## Slide 1: Embedded module for detection and recognition of miniature traffic signs using neural networks
Student: Mihai-Bogdan Bindila
Mentors: Cosmin Lazar and Mihai Negru

## Slide 2: Contents
Context - Bosch Future Mobility Challenge 2020
Overview
System architecture
Dataset preparation
Convolutional Neural Network architecture
Network training
Model conversion for inference in C++
Pipeline
Preprocessing 1
Pipeline for pole extraction
Preprocessing 2
Prediction
Results
Conclusions
References

## Slide 3: Context - BFMC 2020
-> The module is a component of the car with which the Back On Track team will compete at BFMC 2020.
-> The car is built on a 1/10 scale.
-> The car must be autonomous.
-> The algorithm will run on a Raspberry Pi 4 Model B - 4GB.
-> There is a serial connection between the Raspberry Pi and a Nucleo F401RE microcontroller.
-> The microcontroller operates the car according to the messages received from the Raspberry Pi.

## Slide 4: Context - BFMC 2020
-> The rest of the algorithms that must be implemented are:
- Line keeping
- Object avoidance
- Side parking
- Track completion guided by a GPS
- Pedestrian and ramp detection

## Slide 5: Overview
-> The module runs on an embedded system with limited resources.
-> The ROI detection algorithm was prototyped in Python and rewritten in C++ for efficiency. The OpenCV library was used for image processing.
->Detection is based on two pipelines that run in parallel:
- the first one is based on pole detection
- the second one is used as a backup solution and generates a color-based segmentation
-> A feed-forward neural network developed in Tensorflow and Keras classifies ROIs.
-> The algorithm is fully autonomous, thus is no need for calibration of the parameters for different scenarios.
Notes: czzzjzj

## Slide 6: System architecture

## Slide 7: Dataset preparation - sources of images and pipeline
-> The images come from 3 sources: - clips received from the contest organizers
- clips recorded in various locations
- German Traffic Sign Benchmark dataset
->The images from the first two sources were captured with Raspberry Pi Camera v2.1. The algorithm for ROIs detection has extracted the areas of interest.

## Slide 8: Dataset preparation - augmentation
->The images were divided into the training set and the test set. Image classes are stop, parking, priority road, pedestrian crossing and others.
-> In terms of augmentation, the ImageDataGenerator from the Keras API was used. The transformations applied are scaling, rotations, zoom-in, zoom-out, changes in brightness and shift of color channels.
-> After augmentation, there are 950 images for training and 350 images for testing in each class.
Augmentation example
->

## Slide 9: Dataset preparation - preprocessing
-> Preprocessing consisted of resizing images to 64x64 pixels, followed by a grayscale conversion and applying a contrast limited adaptive histogram equalization (CLAHE).
-> For the last operation different values of the pixel patch size were tried, but the best results were obtained for 8x8 pixels patches.
-> Applying a histogram equalization on the images of the dataset brings a boost to the accuracy of the network, as demonstrated in the paper [1].
CLAHE with different sizes of the patch

## Slide 10: Convolutional Neural Network architecture
-> A feed-forward convolutional neural network is used. It has 3 principal types of layers: convolution, max pooling and fully connected. To avoid overfitting there are two dropout layers with a value of 0.5. Batch Normalization was used to allow higher learning rates..

## Slide 11: Convolutional Neural Network architecture
-> The activation function for the last layer is Sigmoid, which replaces the classic Softmax. The loss used is a binary cross-entropy, so the problem becomes a classification of type one versus all.
-> It turns out that the prediction is no longer represented by a probability distribution with the sum equal to 1, instead each class can has a probability between 0 and 1.
-> A prediction is considered correct if the highest probability out of the 5 is greater than 99%.
-> The network has just 89,381 parameters compared to similar networks like MobileNetV2 that has 3.4 millions.

## Slide 12: Network training
-> For training the best results were obtained using a batch of 16 images and the Adam optimizer. The learning rate was set to 3e-5 and was decayed by 2% from each current value.
-> Overfitting was eliminated by using dropout layers and by monitoring the monotony of the loss function and using the early stopping technique.
-> For model selection grid search was used.
-> The results obtained are: - 96.24% accuracy for the train dataset
- 95.85% accuracy for the test dataset

## Slide 13: Model conversion for inference in C++
-> Because the model will be used in a module written in C++, a conversion is needed.
-> Initially the model is saved in H5 format which is then converted to JSON format using the Frugally-Deep library.
-> The new model is easy to use in a C ++ code because it only needs 4 header-only libraries to make a prediction based on it.
->Due to the conversion the inference time increases by about 128%.

## Slide 14: Pipeline
-> Images are taken by the camera or from a local folder. The two preprocessing steps are applied in parallel, after which the extracted ROIs are processed and then classified.
-> Finally, the distance to the sign is measured and depending on the detected traffic sign, a message is sent to the Nucleo microcontroller, which will perform a specific action.
-> The two preprocessing steps have 2 common operations:
- resize to 640x480 pixels
- Gamma compression for highlighting details

## Slide 15: Preprocessing 1
-> This preprocessing pipeline has as input the initial image and generates a picture with the edges of the objects.
-> In the resulting image the pillars of the traffic signs will be detected.

## Slide 16: Preprocessing 1 - steps
-> After gamma correction, the following steps are applied:
- Convert BGR color space to grayscale.
- Blur the image with a 5x5 Gaussian filter, with this low-pass filter the weak edges are blurred.
- Apply the Canny filter adaptively for each frame, the threshold value is the same as the threshold value used by the binarization with the Otsu method [2].
- The last step is the application of dilation with 3x3 size to thicken the segments that must be extracted from the image to recognize the pillar.

## Slide 17: Preprocessing 1 - visualization
Initial image Enhanced image
->

## Slide 18: Preprocessing 1 - visualization
Canny edge detector Dilated edges
->

## Slide 19: Pipeline for pole extraction
-> Probabilistic Hough Transform is applied to the preprocessed image to determine the set of segments in the picture.
-> The set of segments is filtered so that in the end only the lines that are most likely to be the edges of the column remain.

## Slide 20: Pipeline for pole extraction
-> The resulting segments are filtered on different criteria, including their angle with the ox axis. It must be between 75 and 105 degrees. At the moment when we approach the column, this inclination appears due to the perspective.
-> Groups are formed with segments that fit one line at a time, and of these, only the one with the minimum y coordinate is retained, which helps us to keep the segment that is most likely to extend to the upper base of the pole.

## Slide 21: Pipeline for pole extraction
-> To implement this component, each segment was colored with a different color and a 5x5 matrix was centered at the top of each segment to determine the neighbors that will be retained by color.
-> The remaining segments are then grouped based on the criteria given by the distance between them, their length and the level on the oy axis at which they are located.

## Slide 22: Pipeline for pole extraction - visualization
Initial set of segments Set of lines after filtering
->

## Slide 23: Pipeline for pole extraction - visualization
Groups of lines

## Slide 24: ROI extraction based on pole
-> Depending on the width of the columns, bounding boxes are extracted and also computed taking into consideration the inclination of the pillar.
-> If there is such an inclination, a translation is applied to the left or to the right for the region of interest.
-> These bounding boxes are filtered based on area and proportionality ratio.

## Slide 25: Preprocessing 2 - steps
-> Convert the image from the BGR color space to HSV because the brightness component is separated from the color components. This property helps us to generate a segmentation that makes an abstraction of the brightness from the environment.
HSV color space

## Slide 26: Preprocessing 2 - steps
-> Apply three masks for red, yellow and blue. After this step, the bounding boxes of the connected components are generated.
-> These regions of interest are filtered by area and aspect ratio.
Mask for blue color Extracted ROIs ROIs after filtering

## Slide 27: Prediction
-> For each extracted ROI, the following operations must be applied:
- resize to 64x64 pixels
- grayscale conversion
- contrast limited adaptive histogram equalization which is applied on 8x8 pixel patches
-> These preprocessed ROIs are then classified and if the highest probability of the 5 classes is over 99%, then it is considered a correct prediction.
-> The prediction of the traffic signs extracted on the basis of the color information is verified taking into account this information.

## Slide 28: Results- performance
-> The algorithm was tested on a laptop with the following specifications:
-> Intel i7 7700hq processor
-> 8GB RAM
-> HDD with 5400 rpm
-> The images are read from the hard disk, 23 fps were obtained in the worst-case scenario, namely in pictures in which there were many regions of interest extracted and classified.
-> If the algorithm runs in scenarios in which all traffic signs have visible poles, then the frame rate increases to 39, due to stopping the color-based segmentation component.
-> If both pipelines are running, on a Raspberry Pi 4 the algorithm runs at 6-10 fps.

## Slide 29: Results - special scenarios
-> The column is not visible even if a lighting factor of 75% is applied.
Detection based on color Lighting increased by 75%

## Slide 30: Results - special scenarios
-> There is no accurate representation of colors.
Incorrect color representation
->
->

## Slide 31: Results - special scenarios
-> There are partial occlusions of the traffic sign.
"STOP" occlusion

## Slide 32: Results - real-time predictions

## Slide 33: Conclusions
-> In conclusion, this module represents a robust solution for detecting and recognizing miniature traffic signs.
-> Due to the implementation in C++, the algorithm is optimized for embedded systems.
-> Because there are two methods of extracting ROIs, the algorithm will work in scenarios where colors are not represented correctly or the pole of the traffic sign is not visible.
-> The idea of detecting traffic signs based on the pole is a new idea, and due to the configurable parameters of the algorithm it can be scaled for real scenarios.
-> Recognition based on a neural network brings flexibility to the solution, the operation being robust even in conditions with uncontrolled brightness of the environment.

## Slide 34: References
[1] P. Sermanet and Y. LeCun, "Traffic sign recognition with multi-scale Convolutional Networks,"
The 2011 International Joint Conference on Neural Networks, San Jose, CA, 2011, pp. 2809-2813.
[2] Fang, Mei & Yue, GuangXue & Yu, QingCang. (2009). The Study on An Application of Otsu Method in
Canny Operator.

## Slide 35: Thank you for your attention!